## Slide 1
esp32_lua_llm · architecture walkthrough · 2026-09
ESP32-S3 · NIMBLE · LUA 5.4 · USB CDC · LLM HOST
A BLE test lab on a USB dongle,
operated by an LLM.
Passive sniffing, on-device Lua scripting, and a host-side agent that reads the traffic, writes its own tools — and ships them to the dongle over USB.
v1.1.0 · stages 0–5 complete · stage 6 (agent platform) in progress on Lua_tool_extension_dev
PC — LLM host tools
USB CDC
ESP32-S3 dongle
2.4 GHz
BLE adverts &
GATT peers
Notes: One-sentence pitch: a $5 ESP32-S3 sniffs BLE and runs Lua; a Python host application puts an LLM in the loop. Everything in this deck is live-verified on hardware. v1.1.0 released; stage 6 (the agent platform) is the current branch.

## Slide 2
00 · MOTIVATION
Why this project exists
Sniffing BLE is heavy
Proprietary capture hardware, Wireshark, and a fresh one-off parser script for every device you meet.
Firmware logic is frozen
Every filter tweak or new payload format is a rebuild–reflash–retest cycle on the bench.
A human sits in every loop
Someone has to read the capture, spot the pattern, and write the next probe script by hand.
Put a Lua sandbox on a $5 radio — and hand the keyboard to an LLM.
The dongle keeps watch, the model reads the traffic, and new tooling ships over USB in seconds — not reflash cycles.
THE CLOSED LOOP — ALREADY RUNNING LIVE
capture
JSON lines
analyze
LLM reads
generate
Lua tool
deploy
USB · sandboxed
observe
next scan
…and the next iteration can use the new tool
02
Notes: Frame the pain first (3 rows, left), then the idea (card, right): Lua on device + LLM on host = extensible instrumentation without reflash. The bottom loop is the structure of the whole talk — capture, analyze, generate, deploy, observe.

## Slide 3
SYSTEM · 10,000 FT
System at a glance
HOST PC
Cloud LLM — OpenAI-compatible
Qwen (DashScope) active today · DeepSeek, OpenRouter, Ollama drop-in
Host tools — Python, ~2.8k lines
llm_loop.py · run_case.py · assistant.py, deliberately self-contained
Test suites
Unity C 126 · pytest 151 · one-command hardware gate run_all_hw.py
text commands
USB CDC
JSON lines ≤512B
tagged with cmd
ESP32-S3 DONGLE
NimBLE observer —
passive, continuous scan
Scan pipeline —
parse → filter → hook → JSON
Lua 5.4 sandbox —
128 KB static pool
CONN central (opt.) —
one GATT peer
BLE · 2.4 GHz
adverts from
any nearby device
one GATT peer —
notify or polled
The dongle never exposes BLE toward the host — host traffic rides USB only; the radio is the product. Every box on this slide is a later slide.
03
Notes: The one map to keep: PC on the left (cloud LLM + three Python tools + tests), USB CDC in the middle (commands out, JSON lines back), dongle on the right with its two radio roles: passive observer and optional GATT central. Point forward: each container gets its own section.

## Slide 4
01 · DONGLE FIRMWARE
Nine components, ~5.7k lines of authored C
USB console
166 L · firmware/components/usb
USB-Serial/JTAG line I/O; the Ctrl+C interrupt path.
Storage
174 L · firmware/components/storage
LittleFS — 8 KB script slot at /littlefs/script.lua.
BLE scan
355 L · firmware/components/ble
NimBLE observer; FNV-1a dedup in a ~1 s window.
BLE conn
1,110 L · firmware/components/ble
optional GATT central; subscribe with poll fallback.
AD parser
217 L · firmware/components/ad
decodes AD structures: name, UUIDs, manufacturer data.
JSON encoder
739 L · firmware/components/json
one line per event, ≤512 B, all dynamic text escaped.
Filter engine
246 L · firmware/components/filter
up to 16 C rules evaluated on the hot path.
Lua + pool
962 L · firmware/components/lua
Lua 5.4 sandbox; 128 KB static pool allocator.
Also on the die: CLI 978 L — command dispatch + IDLE / SCANNING / SCRIPT_RUNNING state guards · bridge 254 L — per-line sandbox scan on script upload · power 187 L — auto light sleep with PM locks.
main.c init chain → usb → storage → cli → ble → [conn] → pipeline → lua → bridge → power
+ ~29k lines of vendored Lua 5.4 (unmodified upstream) — full firmware tree ≈35.8k lines. Modules talk only through interfaces/*_if.h headers (~1.2k lines).
04
Notes: Nine components, one rule: modules communicate only via the interfaces/ headers — that contract layer is why parallel AI agents could extend this codebase without stepping on each other. Line counts are real (cloc-style from the repo).

## Slide 5
01 · DONGLE FIRMWARE
One packet's journey: radio to JSON line
SCAN PLANE — EVERY ADVERT IN RANGE
NimBLE observer
always scanning
Dedup
FNV-1a · ~1 s
AD parse
proto layer
C filter
≤16 rules
Lua on_adv
keep / drop
JSON encode
≤512 B line
USB TX
one mutex
CONN PLANE — ONE GATT PEER, OPT-IN (F2.4)
GATT connect
by UUID or address
6 s timeout · 5 retries
subscribe
notify / indicate
no CCCD?
→ poll reads
100–10 000 ms
payloads tagged
from_poll
re-stream as
{"src":"conn"} lines
INVARIANTS
zero-malloc hot path — static buffers end to end
state guards −911:
IDLE / SCANNING / SCRIPT_RUNNING
Ctrl+C (0x03) breaks in anywhere — even mid-poll
one TX mutex — output lines never interleave
Scan plane runs in one pipeline task (prio 2); the CLI task (prio 5) stays responsive through all of it. The conn plane is a separate worker task (4 KB stack).
05
Notes: Walk one advert left to right: radio → dedup → parse → filter → Lua hook → JSON → USB. Then the second plane: an optional GATT connection whose subscribe can degrade to polling — that fallback is what the first_order_poll demo exercises. Close with the invariants; they are why the thing never falls over.

## Slide 6
02 · BLUETOOTH & USB
Two planes: BLE toward the world, USB toward the host
BLE · 2.4 GHz — toward the world
Passive observer
continuous discovery on BLE_HS_FOREVER — sees every device without connecting.
Optional central (F2.4)
opt-in via Kconfig; connects by advertised service UUID or direct address.
Subscribe, then poll
notify / indicate first; if the CCCD write fails, GATT reads every 100–10 000 ms.
Deterministic teardown
CONN STOP returning ok ≠ off — hosts wait for CONN STATUS state:"off".
USB · CDC 115200 — toward the host
Lines in
plain text commands; CR, LF, or CRLF line endings all accepted.
Ctrl+C = interrupt
0x03 is polled even inside the conn worker — no command can lock the CLI.
JSON lines out
one object per line, ≤512 B, serialized through a single TX mutex.
Keep the port open
closing COM12 toggles USB power and resets the chip (ESP_RST_USB, note N3).
Both planes share one CLI dispatcher and one error model — hosts react programmatically instead of parsing prose.
06
Notes: Key correction this slide makes for most audiences: BLE is NOT the host link. The dongle's radio talks to other devices; the host link is USB CDC. Left = radio behaviors (passive + optional central), right = the USB contract details that host tools rely on.

## Slide 7
02 · BLUETOOTH & USB
The wire contract: text lines in, JSON lines out
HOST
DONGLE
SCAN START\r
{"cmd":"scan","status":"ok","state":"SCANNING"}
SCRIPT LOAD → paste Lua lines → SCRIPT END
{"cmd":"script","status":"loaded"} · per-line sandbox scan → −612 on reject
ERROR MODEL — EVERY MODULE OWNS A 100-WIDE NEGATIVE RANGE
ADV −1xx
JSON −2xx
FILTER −3xx
BLE −4xx
USB −5xx
LUA −6xx
FS −7xx
PIPE −8xx
CLI −9xx
Every response carries its cmd, so hosts match answers to questions even when lines arrive stale — 76 CLI responses are strict-JSON-validated by tests.
07
Notes: This is the whole protocol on one slide: four exchanges cover scan control and script upload. The cmd field is the anti-stale-line trick — after a Ctrl+C interrupt, old responses can't be mistaken for new ones. Error ranges mean the host can branch on the module that failed.

## Slide 8
03 · LUA TOOL REGISTRY
H6.1 · A tool pack is just a Lua file
-- host_app/tool_packs/demo.lua
-- private globals carry the pack prefix
demo_t0 = nil
-- every tool: ONE table arg, returns a string
function mean(a)
local s = 0
for _, v in ipairs(a.numbers) do
s = s + v
end
return string.format("%.3f",
s / #a.numbers)
end
-- manifest(): JSON, one piece per line
function manifest()
return '{"version":1,"name":"demo",'
.. '"tools":[{"name":"mean", …]}'
end
One statement per line, ≤240 B
packs ride the existing LUA EXEC path unchanged — zero firmware changes in M1.
manifest() is the API surface
name, doc, typed args, returns, mutating flag, example — fetched in 180 B chunks (8 KB budget).
One table argument, always
mean({numbers = {3, 5, 10}}) — the system prompt teaches the model this exact shape.
The registry is host-side
/tools caches manifests authoritatively; refresh detects a device reset and clears stale entries.
3 demo tools
tests 79 → 108
0 firmware changes
Loads are RAM-only (LUA EXEC run mode) and confirm-gated — nothing persists to LittleFS until milestone M2 (design decision 14).
08
Notes: The registry's cleverness is that it added a whole extension mechanism with zero firmware changes: a pack is a plain Lua file obeying two constraints (one statement per line ≤240 B; manifest() describing each tool). The demo pack ships mean, temp_convert, bench_reset.

## Slide 9
03 · LUA TOOL REGISTRY
From /tools to a cap-3 execution loop
REGISTRATION — /tools refresh
/tools refresh
host asks the device
LUA EXEC return
string.sub(manifest(), i, j)
180 B chunks
host validation
strict JSON · no reserved
or duplicate names
collision check — duplicate
packs & tool names rejected
BEFORE any line is sent
[y/N] confirm
loaded to RAM only
GENERATE-AND-EXECUTE — INSIDE ONE USER TURN
user asks a question
about live traffic
LLM composes a tool
program from the registry
host runs it line-by-line
on the dongle
result: tool> 6.000
fed back to the model
each result informs the next program
CAP 3 — at most three consecutive executions per turn, then one corrective round forces a plain answer. A device error (e.g. sandbox −612) becomes the model's next hint instead of a crash.
Live-verified 2026-09-03 — first real-hardware runs caught a stray brace and a nan-convention bug (evidence logs in harness/02-knowledge/). Programs defining on_adv / transform / manifest still take the human deploy gate.
09
Notes: Top row: how a pack registers — the host pulls the manifest in chunks, validates strictly, and rejects name collisions BEFORE sending anything to the device. Bottom: the agent loop the LLM actually runs — compose, execute, read result, iterate — capped at three consecutive executions per turn so the model can't runaway-loop; then it must answer in plain text.

## Slide 10
04 · HOST LLM APPLICATION
Three self-contained Python tools
llm_loop.py
H5.1 · 486 lines
capture / analyze / deploy / loop — one subcommand each
caps prompts at 30 deduplicated lines to bound token cost
--dry-run works fully offline, no key needed
run_case.py
H5.2 · 813 lines
scenario harness + a controlled GATT peer on the PC (WinRT)
--estimate: the LLM's JSON answer is checked against physics
first_order & first_order_poll cases with ground-truth verdicts
assistant.py
H5.3 + H6.1 · 1,544 lines
interactive REPL over the live dongle, both planes drained
typed envelopes: answer · lua · clarify · error
/scan /conn /deploy /tools — sessions tee'd to timestamped logs
DEPLOY SAFETY CHAIN — WHAT HAPPENS TO EVERY GENERATED SCRIPT
LLM replies
{type:"lua", code}
host parses —
strict JSON · one retry
human gate
deploy? [y/N]
SCRIPT LOAD —
per-line sandbox scan
device gate
−612 = reject
The three tools deliberately share conventions but zero code — parallel AI sessions can build features on disjoint branches without collisions.
10
Notes: llm_loop = batch pipeline; run_case = reproducible scenario harness with a simulated plant; assistant = the interactive product. Emphasize the safety chain at the bottom: nothing the LLM writes reaches the radio without strict parsing, a human y/N, a per-line sandbox scan, and the on-device -612 gate as the last word.

## Slide 11
04 · HOST LLM APPLICATION
One client, any OpenAI-compatible provider
CONFIG — .llm_env (gitignored)
Provider-agnostic
any /chat/completions endpoint: OpenAI, DashScope (Qwen — active today), DeepSeek, OpenRouter, local Ollama.
Env wins as a unit
if the shell has any LLM_* variable, the whole config comes from env; otherwise the file — never mixed. Mixing = guaranteed 401 (observed).
Thinking off by default
QWEN_ENABLE_THINKING=false — reasoning models stall >180 s on script-generation prompts.
POST /chat/completions
PATH A · AUTH
PATH B · WRONG DIALECT
401 — key rejected
one announced retry on .llm_env credentials
✓ 200 — session continues
404 — base ends /api/v1
heal to /compatible-mode/v1, retry once
✓ 200 — new base sticks for the session
Read timeouts are caught and surfaced as an envelope type:error — the session survives every provider hiccup.
All three host tools self-heal identically — the convention is copied, not shared (same isolation rule as slide 10).
11
Notes: Boring but battle-tested: the provider layer survived four .llm_env rewrites. Two self-heals — auth fallback to the file, URL dialect fix for Aliyun's native endpoint — plus thinking-mode off. The env-wins-as-a-unit rule exists because mixing an ambient key with the file's base URL is a guaranteed 401.

## Slide 12
04 · HOST LLM APPLICATION
The loop closes on real hardware: first-order plant
PC simulates plant
y′ = (K·u − y) / τ
PC serves it over
WinRT GATT
dongle auto-connects
by service UUID
re-streams {"src":"conn"}
JSONL — 60/60 lines
LLM returns JSON
estimate of τ
host checks vs
ground truth
FIRST_ORDER_POLL — THE DONGLE MUST POLL; NOTIFICATIONS DISABLED
9.5
τ̂ — the LLM's estimate, from raw JSONL alone
true τ = 10.0 · error −5 %
±10 % tolerance → PASS
60 / 60 conn lines captured — zero drops
ground truth: 63.2 %-of-K settling rule
notify variant (first_order) passes the same gate
Live run, Aug 2026 — capture JSONL and transcript archived under harness/02-knowledge/ (README: host cases).
12
Notes: The money slide. A first-order plant (tau=10) is simulated on the PC and served over GATT; the dongle must poll because notifications are off. 60 of 60 lines captured, and the LLM's estimate of tau from raw samples: 9.5 against a true 10.0 — inside the 10% tolerance. Physics-checked, not vibes.

## Slide 13
05 · HARNESS & WORKFLOW
From C unit tests to a one-command hardware gate
Chart: 
| Unity C (host-built) | assistant (pytest) | HW · conn (GATT) | HW · BLE+Lua | run_case (pytest) | HW · bridge | HW · power | HW · peer | llm_loop (pytest)
checks | 126 | 108 | 65 | 45 | 33 | 32 | 14 | 11 | 10
THE HARDWARE GATE — ONE COMMAND
python tests/hw/run_all_hw.py
assert firmware VERSION first — wrong build stops everything
6 suites as subprocesses — transcripts teed to evidence/<ts>/
after EACH suite: reset_reason must be 11 (USB) or None
all green = the merge gate
Unity C 126 = 108 unit + 10 response-contract + 8 fuzz — the fuzzer's first run found 3 real encoder defects. Soaks (2 h adv, conn reconnect every 300 s) run outside the gate. Source: tests/README.md · BRANCH.zcode.md.
13
Notes: Left: the whole check inventory as one chart — C tests host-built with gcc, pytest suites for each host tool, and five hardware suites driven over the real COM port. Right: the hardware gate. The subtle detail is the reset_reason check after EVERY suite — if the chip rebooted for any reason other than USB replug, the gate fails.

## Slide 14
05 · HARNESS & WORKFLOW
Quality was earned the boring way
Fuzz from day one
deterministic LCG inputs through both JSON encoders, a strict-JSON oracle, and every small buffer size.
3
real encoder defects
found & fixed
Golden transcripts
frozen real device noise — ANSI NimBLE logs, CLI echoes, boot lines — replayed as fixtures; tripped a real stale-line weakness.
76
CLI responses strict-JSON
re-validated
Soak
2 h advertisement soak watching the Lua pool for fragmentation; conn soak tearing down and reconnecting every 300 s.
2 h+
adv soak + conn soak,
no leaks, no drift
The ledger
every evaluation logged and re-run per stage: 30+6 initial findings → 28 all-stage → 7 at v1.0.0 → all resolved; sessions file evidence in harness/02-knowledge/.
ALL
EVAL FINDINGS
RESOLVED
Numbers from bug_check/README.md, tests/README.md and FEATURES.zcode.md.
14
Notes: The theme: no quality claim without an artifact. The fuzzer paid for itself on its first run; golden transcripts keep real-world noise in CI; soaks watch for long-horizon decay; and the ledger means every bug class found by an evaluation round is provably closed before the next stage.

## Slide 15
05 · HARNESS & WORKFLOW
Feature workflow: proposals, branches, manifests, evidence
feature branch + BRANCH.zcode.md
squash merge
registered baseline
v1.1.0
one feature per branch · cut from a registered baseline · never commit to a baseline directly
1
Design-first proposal
docs/feature-proposal-*.md with numbered decisions — 14 of them for the tool registry.
2
Cross-agent review
a second model (deepseek) reviews the proposal and the code before anything merges.
3
Branch from a registered baseline
BRANCH.zcode.md tracks ACs, verification plan, changelog — no manifest, no merge.
4
Implement with evidence
tests plus live-verification logs filed under harness/02-knowledge/.
5
Squash merge, keep the branch
manifest deleted in the squash, FEATURES.zcode.md index updated, branch kept as the revert path.
Commits follow type(scope): summary + What / Why / How / Verification sections — enforced by a commit-msg git hook.
15
Notes: Process as architecture: the branch diagram is the git model — baselines only receive squash merges, feature branches carry a manifest that doubles as the merge contract. The five steps on the right are the lifecycle every feature walks; H6.1 (the tool registry) is the first feature to run the full ritual end to end.

## Slide 16
05 · HARNESS & WORKFLOW
Built by AI agents — what actually worked
A context layer written for machines
CLAUDE.md brief · harness/00-global-context specs · 02-knowledge process reports
“Context engineering beats prompt engineering”
Martin Fowler, 2026
Narrow agents on disjoint branches
the three host tools share conventions, zero shared code
“Single-responsibility agents outperform do-everything ones”
field reports, 2026
Models reviewing models
deepseek reviews proposals and implementations pre-merge
“Adoption is easy — trust is the bottleneck; review everything”
Graphite guide, 2026
Evidence gates, not vibes
the HW gate + evidence logs decide merges; sessions answer “were the docs sufficient?”
“90 % use agents weekly — only 29 % trust the output”
JetBrains · Uvik, 2026
90 %
use agents weekly — JetBrains 2026
2.3×
merge rate for heavy users — LinearB 2026
29 %
trust the output — Uvik 2026 · why we gate on evidence
Links in slides_outline.zcode.md — martinfowler.com, agents.md, JetBrains / LinearB / Uvik 2026 research.
16
Notes: This project is also a case study in AI-assisted development. Left column: what we actually did. Right column: what 2026 research says — the mapping is close, which is the point. The 29 % trust stat motivates the whole evidence-first workflow: never merge on vibes, merge on the hardware gate.

## Slide 17
esp32_lua_llm · what's next
Where it's headed
M2 · Persistent packs
tool packs live in LittleFS slots and auto-register on boot — survive power cycles.
M3 · hw.* bindings
Lua tools reach GPIO, UART, energy profiling — the dongle becomes an actor, not just an observer.
M4 · Native function-calling
the assistant drops envelope parsing for real tool calls; the registry exposes itself over GATT.
Also queued: CONN STOP settle semantics · full battery + coverage pass · push master to origin.
The dongle captures. The model thinks.
The loop closes.
~5.7k LOC authored firmware (35.8k with vendored Lua 5.4) · ~2.8k Python host tools · 126 Unity C tests
108 + 33 + 10 pytest · 167 hardware checks · τ̂ 9.5 vs τ 10.0 · v1.1.0
E:\agent\esp32_lua_llm · Lua_tool_extension_dev → master (review pending)
Notes: Close on trajectory: M2 makes tools persistent, M3 turns the dongle into an actor, M4 makes the LLM integration native. Then the one-liner and the numbers strip. Q&A prompts: what would you sniff first?